IOP-SANFO-241509008

2.4GHz 15dBi Sector Antenna

| Electrical Specification |
| --- |
| Frequency range | 2400MHz – 2500MHz |
| Gain | 15 dBi |
| VSWR | 1.5 : 1 Max. |
| Polarization | Linear, Vertical |
| HPBW / Horizontal | 90° |
| HPBW / Vertical | 8° |
| Electrical downtilt | 0° |
| Power handing | 5W (cw) |
| Impedance | 50 Ohms |
| Connector | N Jack |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -40℃ to +80℃ |
| Humidity | 95% @ 55℃ |
| Radome color | Gray |
| Radome material | ABS, UV resistant |
| Weight | 1000g |
| Dimensions | 900 × 88 × 70 mm |