IOP-GANFO-542600609

5GHz 26dBi Grid Antenna

| Electrical Specification |
| --- |
| Frequency range | 5470MHz – 5725MHz |
| Gain | 26 dBi |
| VSWR | 1.5 : 1 Max. |
| Polarization | Horizontal, Vertical |
| HPBW / Horizontal | 6° |
| HPBW / Vertical | 9° |
| Front to back ratio | 25dB |
| Power handing | 100W (cw) |
| Impedance | 50 Ohms |
| Connector | N Jack |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 241Km/hr (Operational) |
| Temperature | -40℃ to +80℃ |
| Humidity | 95% @ 55℃ |
| Radome color | Gray - white |
| Radome material | UV resistant , Aluminum Die Cast |
| Weight | 2.5Kg |
| Dimensions | 40 x 60 cm |