IOP-OANMO-580536025

5GHz 5dBi Omni Antenna

| Electrical Specification |
| --- |
| Frequency range | 4900MHz – 5900MHz |
| Peak gain | 7.0 dBi |
| Average gain | 5.0 dBi |
| VSWR | 2 : 1 Max. |
| Polarization | Linear, Vertical |
| HPBW / Horizontal | 360° |
| HPBW / Vertical | 25° |
| Power handing | 2W (cw) |
| Impedance | 50 Ohms |
| Connector | N Plug |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -40℃ to +70℃ |
| Humidity | 95% @ 55℃ |
| Radome color | Gray |
| Radome material | ABS |
| Weight | 70g |
| Dimensions | Φ22 × 183 mm |