IOP-PANFO-582300909

5GHz 23dBi Panel Antenna

| Electrical Specification |
| --- |
| Frequency range | 5725MHz – 5875MHz |
| Gain | 23 dBi |
| VSWR | 1.5 : 1 Max. |
| Polarization | Linear, Vertical / horizontal |
| HPBW / Horizontal | 9° |
| HPBW / Vertical | 9° |
| Front to back radio | 40dB |
| Power handing | 20W (cw) |
| Impedance | 50 Ohms |
| Connector | N Jack |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -40℃ to +80℃ |
| Humidity | 95% @ 55℃ |
| Lightning protection | DC ground |
| Radome color | White |
| Radome material | ABS, UV resistant |
| Back plate material | Power-coating iron |
| Weight | 1600g |
| Dimensions | 360 × 360 × 16 mm |