IOP-PANFO-5D2001010

5GHz 20dBi Dual Polarization Panel Antenna

| Electrical Specification |
| --- |
| Frequency range | 5150 – 6100MHz |
| Gain | 20 dBi |
| VSWR | 2 : 1 Max. |
| Polarization | Dual Linear, +- 45° |
| HPBW / Horizontal | 10° |
| HPBW / Vertical | 10° |
| Standard compliance | N / A |
| Front to back ratio | -30dB (Max) |
| Isolation | 24dB (Min) |
| Power handing | 20W (cw) |
| Impedance | 50 Ohms |
| Connector | N Jack × 2 |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -40℃ to +80℃ |
| Humidity | 95% @ 55℃ |
| Lightning protection | DC ground |
| Radome color | Gray |
| Radome material | PC, UV resistant |
| Weight | 1100g |
| Dimensions | 320 × 320 × 20 mm |
| Waterproof | IP-X5 |
| Mounting kit | Pole mount & Wall mount |

*exclusive of mounting kit